Computational Intelligence COM907M1
Tutorial 1

In the field of hydrology, the study of rainfall patterns is most important. The rate of rainfall, in units of mm/h, falling in a particular geographic region could be described linguistically. Defining membership functions for linguistic variables ‘heavy’ and ‘light’ as follows

      Develop membership functions for the following linguistic phrases
1. More or less light
2. Heavy but Not very heavy
3. More or less light but not very heavy

2. Let A be a fuzzy set in X defined as

 and given is the fuzzy relation R in via the following relational matrix:

What will be the fuzzy output B in Y using max-min operation?

In a car breaking simulation systems, load on a car is described by the following MFs.

Figure 2.1: MFs load

Define the following labels which have linguistic hedges appended to the fuzzy label Small and Large defined above. Express the following graphically
1. Small but very large
2. Small or very large

Computational Intelligence COM907M1
# Tutorial 2

1. Consider the following Takagi-Sugeno rules:

If x is A1 and y is B1 Then
If x is A2 and y is B1 Then
If x is A1 and y is B2 Then
If x is A2 and y is B2 Then

The antecedent fuzzy sets are

Compute the value of z for and where z is defined as

are the firing strength of the rules

2. Consider the classical control problem of an inverted pendulum.

Figure 2.1: Inverted Pendulum.

Where  displacement and  control torque. Assuming and equivalent to state-variables and by linearising for the small , we arrive at the following discrete form of the inverted pendulum system

The universes of discourse are , and . In order to develop a Mamdani-type fuzzy control system, x1, x2 and u are considered as inputs and output respectively. The membership functions for x1, x2, and u are defined in the following figures.

Figure 2.2: MFs for x1, x2, and u

The rule-base for the fuzzy system is represented by 9 rules shown in the table below

Table 2.1: Rule-base for Mamdani-type FLC
x1	x2
	P	Z	N
P	PB	PS	Z
Z	PS	Z	NS
N	Z	NS	NB

Develop a fuzzy control system for the inverted pendulum problem (block diagram). Taking initial conditions x1(0) =1 and x2(0) = -2.5/s, demonstrate graphically one iteration of simulation of the fuzzy control system. Use estimates in any defuzzification procedure to be used.

3.A steam engine simulation system has been developed using Tsukamoto rule, where x represents speed, y represents pressure and z represents throttle position. Table 3.1 describes the rule base of the system.

Table 3.1: Rule-base for the Sugeno-type FLC
x @ speed	y @ pressure
	B1	B2
A1	C1	C2
A2	C2	C1

Where throttle positions are defined by monotone membership functions C1, and C2. The fuzzy sets for speed and pressure are described by the membership functions in Figure 3.1-2 and monotone membership functions for C1, and C2 are defined in Figure 3.3.

Compute the throttle position z at speed and pressure using the Tsukamoto system described above.

Figure 3.1-2: MFs for x and y.
Figure 3.3: MFs for z

Computational Intelligence COM907M1
# Tutorial 3
1. An unknown system is to be modelled. The system has 4 inputs and single output. By inputting 3 sets of random signals 3 responses are measured. The inputs are given as follows:

, ,
The responses for x1, x2, and x3 are d1=-1, d2=-1, and d3=1 respectively. Explain how the system can be modelled by using a Neural Network. Suppose, the model of the system is given by a single neuron network as shown in Figure 7.

Figure 7: Single neuron network.

The initial weight vector is . The learning rate is assumed to be =0.1. To train the network by using delta learning rule, it requires the value of be computed each time which is defined as

where and O are the continuous activation function and output respectively. What will be the weight update () after 2nd iteration of learning using delta-learning rule.

2. Assume the neural network with a single neuron shown in Figure below having the initial weight vector w1, three input vectors and desired outputs as
, ,
The network needs to be trained with a learning constant =1. The activation function is defined as . Show the weight update rule with a diagram.
What will be the weight vector after 2nd iteration of Widrow-Hoff learning? (done in lecture)

3. What are the problems that may occur while training a feedforward neural network using Backpropagation algorithm? What corrections are made to learning rule to overcome these problems? Explain with a diagram.

Computational Intelligence COM907M1
# Tutorial 4
1. Assume the neural network with a single bipolar binary neuron shown in Figure below having the initial weight vector w1, and three input vectors x1, x2, and x3 as

, , and

The network needs to be trained with a learning constant c=1. The activation function is defined as

Show a single iteration of Hebbian learning with a diagram and calculate the weight update.
2. Explain the Kohonen’s Self-Organising Maps (SOM) algorithm.
3. Elman and Hopfield networks are both recurrent networks. Explain the basic differences between the two architectures.